## Slide 1
WSQ COURSE SLIDES
Basic Urban Farming with Hydroponics
Course Code: TGS-2025053916
Version 2.0 · 29 August 2026
Tertiary Infotech Academy Pte Ltd UEN 201200696W
Root-zone control • safe operations • Singapore cases

## Slide 2
TRAINER PROFILE
Your Trainer
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
2
TA
GENERAL TRAINER PROFILE · COMPLETE BEFORE DELIVERY
Name and preferred form of address
Relevant urban-farming / hydroponics experience
Training and Adult Education credentials
Site emergency and escalation role

## Slide 3
TRAINER PROFILE
Dr Alfred Ang
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
3
AA
COURSE LEAD · TERTIARY INFOTECH ACADEMY
WSQ trainer and courseware lead
Focus: mechanisms, measurements and evidence
Ask about system selection and troubleshooting
Escalation: assessment and course administration

## Slide 4
COURSE BRIEFING
Download Course Material
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: lms-tms.tertiaryinfotech.com
4
ANCHOR: sign in → open enrolled course → download current files
• Open lms-tms.tertiaryinfotech.com using your authorised learner account.
• Select this enrolled course and open the Course Material panel.
• Download the current Learner Guide and Activities; report access errors without sharing credentials.
1
Open lms-tms.
→
2
Select this enrolled course and open the Course Material panel.
→
3
Download the current Learner Guide and Activities; report access errors without sharing credentials.

## Slide 5
COURSE BRIEFING
Digital Attendance at Start
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: tertiarycourses.com.sg
5
ANCHOR: identity → attendance event → confirmation
• Use only the provider's authorised attendance channel.
• Confirm the correct course code and session before submitting.
• Never share Singpass, LMS or email one-time passwords.
1
Use only the provider's authorised attendance channel.
→
2
Confirm the correct course code and session before submitting.
→
3
Never share Singpass, LMS or email one-time passwords.

## Slide 6
COURSE BRIEFING
Practice Exam / Knowledge Check
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: exams.tertiaryinfotech.com
6
ANCHOR: course WA-SAQ + observed PP are the assessed instruments
• This is a non-certification WSQ course; revision centres on K1–K4 and A1–A4.
• Use the trainer-provided hydroponics knowledge check and both activity evidence sheets.
• Optional Tertiary practice portal: https://exams.tertiaryinfotech.com/
1
This · non-certification · course · revision · centres · K1–K4
2
trainer-provided · hydroponics · knowledge · check · both · activity
3
Optional · Tertiary · practice · portal · https://exams.tertiaryinfotech.com/

## Slide 7
COURSE BRIEFING
Course outcomes
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: tertiarycourses.com.sg
7
ANCHOR: Perform hydroponic operations to SOP; apply WSH, food-safety, cleaning and maintenance controls.
• K1–K4 equipment, SOP, GAP/WSH, maintenance
• A1–A4 prepare, operate, comply, clean/maintain
1
K1–K4 · equipment · GAP/WSH · maintenance
2
A1–A4 · prepare · operate · comply · clean/maintain

## Slide 8
COURSE BRIEFING
Today's operating flow
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: tertiarycourses.com.sg
8
ANCHOR: Morning theory → lunch → farm tour → kit practice → aquaponics theory → assessment.
• Farm tour and kit practice use checklist PDFs
• 1 hour assessment: WA-SAQ then PP
1
Farm · tour · practice · checklist · PDFs
2
hour · assessment · WA-SAQ · then

## Slide 9
COURSE BRIEFING
Assessment evidence
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: tertiarycourses.com.sg
9
ANCHOR: Competence requires both knowledge and performance evidence.
• WA-SAQ: 4 open-ended questions, 30 min
• PP: one practical task covering A1–A4, 30 min
1
WA-SAQ · open-ended · questions
2
practical · task · covering · A1–A4

## Slide 10
COURSE BRIEFING
Safety stop conditions
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: tertiarycourses.com.sg
10
ANCHOR: Stop and notify the trainer when a condition is unsafe or uncontrolled.
• Damaged electrical equipment or water near unprotected power
• Unknown chemical, missing label/SDS/PPE, unstable structure
1
Damaged · electrical · equipment · water · near · unprotected
2
Unknown · chemical · missing · label/SDS/PPE · unstable · structure

## Slide 11
COURSE BRIEFING
Measurement conventions
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: tertiarycourses.com.sg
11
ANCHOR: Record value, unit, time, instrument and action.
• pH is unitless; EC uses mS/cm or µS/cm
• Temperature and calibration status support interpretation
1
unitless · uses · mS/cm · µS/cm
2
Temperature · calibration · status · support · interpretation

## Slide 12
01
Hydroponic foundations
How water, oxygen, ions and plant demand interact
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
12

## Slide 13
HYDROPONIC FOUNDATIONS
Hydroponics is a controlled root-zone system
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: rhs.org.uk
13
ANCHOR: water + oxygen + ions + support
• Roots obtain mineral ions from a measured nutrient solution, not from soil particles.
• The grower must replace soil's buffering, aeration, anchorage and microbial functions.
• A healthy crop is the output of a balanced root-zone control loop.
1
Roots obtain mineral ions from a measured nutrient solution, not from soil particles.
→
2
The grower must replace soil's buffering, aeration, anchorage and microbial functions.
→
3
A healthy crop is the output of a balanced root-zone control loop.

## Slide 14
HYDROPONIC FOUNDATIONS
The four root-zone variables
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: extension.unr.edu
14
ANCHOR: EC · pH · DO · temperature
• EC estimates total dissolved ionic strength; it does not identify each element.
• pH governs nutrient availability and chemical stability.
• Dissolved oxygen and solution temperature shape respiration and root disease risk.
Legacy visual reused from original slide 22

## Slide 15
HYDROPONIC FOUNDATIONS
Mass balance explains reservoir drift
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: extension.unr.edu
15
ANCHOR: inputs − plant uptake − discharge = change
• Water loss through transpiration can raise EC even when no fertiliser is added.
• Selective ion uptake means a stable EC can still hide nutrient imbalance.
• Top-up, correction and periodic replacement are different control actions.
Local course photo · EC check
+
INPUTS
top-up water + nutrients
−
PLANT UPTAKE
water + selective ions
−
DISCHARGE
drain + sampling losses
=
RESERVOIR Δ
volume + ion profile + EC
Measure trend ≠ diagnose composition

## Slide 16
HYDROPONIC FOUNDATIONS
Root respiration sets an oxygen constraint
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: extension.illinois.edu
16
ANCHOR: warm water holds less dissolved O₂
• Roots consume oxygen to release energy for active ion transport.
• Stagnant warm solution increases hypoxia risk.
• Aeration, return-flow turbulence and lower heat load improve the oxygen margin.
1
Roots consume oxygen to release energy for active ion transport.
→
2
Stagnant warm solution increases hypoxia risk.
→
3
Aeration, return-flow turbulence and lower heat load improve the oxygen margin.

## Slide 17
HYDROPONIC FOUNDATIONS
Capillary and film flow are not interchangeable
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: rhs.org.uk
17
ANCHOR: water depth changes air-filled porosity
• A thin nutrient film preserves a moist, oxygen-rich root surface.
• Deep flooding provides thermal mass but needs active aeration.
• Media pores can wick water while maintaining structural support.
1
thin · nutrient · film · preserves · moist · oxygen-rich
2
Deep · flooding · provides · thermal · mass · needs
3
Media · pores · wick · water · while · maintaining

## Slide 18
HYDROPONIC FOUNDATIONS
Plant water moves down a potential gradient
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: extension.unr.edu
18
ANCHOR: root uptake → xylem → stomata
• Light, heat, humidity and airflow change transpiration demand.
• Roots must supply water fast enough to maintain cell turgor.
• Wilting can occur despite a full reservoir when roots are hypoxic or diseased.
Legacy visual reused from original slide 46

## Slide 19
HYDROPONIC FOUNDATIONS
Nutrient ions are not plant food
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
19
ANCHOR: photosynthesis supplies carbon energy
• Plants build carbohydrates from CO₂ and water using light energy.
• Mineral ions enable enzymes, structure and osmotic regulation.
• More fertiliser cannot compensate for inadequate light or damaged roots.
Legacy visual reused from original slide 48

## Slide 20
HYDROPONIC FOUNDATIONS
Soil-free does not mean risk-free
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
20
ANCHOR: one reservoir can connect every plant
• Recirculation conserves water but can spread a waterborne pathogen rapidly.
• Shared chemistry means one dosing error affects the whole crop.
• Monitoring and sanitation are system controls, not optional housekeeping.
Legacy visual reused from original slide 55

## Slide 21
HYDROPONIC FOUNDATIONS
The production loop is observable
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
21
ANCHOR: setpoint → measure → compare → act → verify
• Define an acceptable band before taking a measurement.
• Use a calibrated instrument and a representative sample.
• Record the correction and confirm the value after mixing.
1
Define an acceptable band before taking a measurement.
→
2
Use a calibrated instrument and a representative sample.
→
3
Record the correction and confirm the value after mixing.

## Slide 22
HYDROPONIC FOUNDATIONS
Evidence distinguishes control from guesswork
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
22
ANCHOR: time-stamped log + calibration + crop response
• A single reading without time, unit and instrument has weak evidential value.
• Trend data reveals drift before visible symptoms appear.
• Crop photographs should show both canopy and roots, not leaves alone.
Legacy visual reused from original slide 66

## Slide 23
02
Hydroponic systems
Select and diagnose flow, support and failure tolerance
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
23

## Slide 24
HYDROPONIC SYSTEMS
Nutrient Film Technique (NFT)
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: rhs.org.uk
24
ANCHOR: shallow recirculating film
• Channel slope and flow continuity are critical; loss of pumping exposes roots quickly.
• Best fit depends on crop mass, root volume, failure tolerance and operator capability.
• Acceptance evidence: even wetting, unobstructed return and healthy white/cream roots.
Legacy visual reused from original slide 75

## Slide 25
HYDROPONIC SYSTEMS
Deep Water Culture (DWC)
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: rhs.org.uk
25
ANCHOR: roots suspended in aerated solution
• Air delivery and raft hygiene govern root oxygen and disease risk.
• Best fit depends on crop mass, root volume, failure tolerance and operator capability.
• Acceptance evidence: even wetting, unobstructed return and healthy white/cream roots.
Legacy visual reused from original slide 80

## Slide 26
HYDROPONIC SYSTEMS
Kratky passive culture
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: rhs.org.uk
26
ANCHOR: static reservoir + deliberate air gap
• A growing air gap supplies oxygen; refilling to the original brim can drown roots.
• Best fit depends on crop mass, root volume, failure tolerance and operator capability.
• Acceptance evidence: even wetting, unobstructed return and healthy white/cream roots.
Legacy visual reused from original slide 87

## Slide 27
HYDROPONIC SYSTEMS
Ebb-and-flow
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: rhs.org.uk
27
ANCHOR: timed flood and drain
• Flood duration wets media; complete drainage restores air-filled porosity.
• Best fit depends on crop mass, root volume, failure tolerance and operator capability.
• Acceptance evidence: even wetting, unobstructed return and healthy white/cream roots.
Legacy visual reused from original slide 91

## Slide 28
HYDROPONIC SYSTEMS
Drip hydroponics
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: rhs.org.uk
28
ANCHOR: emitter uniformity + drainage fraction
• Emitter blockage and uneven pressure create plant-to-plant variability.
• Best fit depends on crop mass, root volume, failure tolerance and operator capability.
• Acceptance evidence: even wetting, unobstructed return and healthy white/cream roots.
emitter uniformity + drainage fraction

## Slide 29
HYDROPONIC SYSTEMS
Aeroponics
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: rhs.org.uk
29
ANCHOR: mist droplet delivery to bare roots
• Fine delivery raises oxygen exposure but creates high sensitivity to nozzle or pump failure.
• Best fit depends on crop mass, root volume, failure tolerance and operator capability.
• Acceptance evidence: even wetting, unobstructed return and healthy white/cream roots.
1
Fine delivery raises oxygen exposure but creates high sensitivity to nozzle or pump failure.
→
2
Best fit depends on crop mass, root volume, failure tolerance and operator capability.
→
3
Acceptance evidence: even wetting, unobstructed return and healthy white/cream roots.

## Slide 30
HYDROPONIC SYSTEMS
Wick systems
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: rhs.org.uk
30
ANCHOR: passive capillary transport
• Low complexity suits small plants; transport rate limits high-demand crops.
• Best fit depends on crop mass, root volume, failure tolerance and operator capability.
• Acceptance evidence: even wetting, unobstructed return and healthy white/cream roots.
Legacy visual reused from original slide 110

## Slide 31
HYDROPONIC SYSTEMS
Dutch bucket
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: rhs.org.uk
31
ANCHOR: individual media containers + common return
• Isolation aids crop support, while a common return retains shared-solution risk.
• Best fit depends on crop mass, root volume, failure tolerance and operator capability.
• Acceptance evidence: even wetting, unobstructed return and healthy white/cream roots.
individual media containers + common return

## Slide 32
HYDROPONIC SYSTEMS
System selection is a constraint decision
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
32
ANCHOR: crop × site × utilities × operator
• Fast leafy greens tolerate different support and cycle times from fruiting crops.
• A rooftop site adds heat, wind, loading and access constraints.
• The simplest system that reliably meets the production target is often the best choice.
1
Fast · leafy · greens · tolerate · different · support
2
rooftop · site · adds · heat · wind · loading
3
simplest · system · that · reliably · meets · production

## Slide 33
HYDROPONIC SYSTEMS
Open and recirculating loops trade risk
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
33
ANCHOR: discharge loss versus shared-reservoir exposure
• Open drain-to-waste operation simplifies chemistry but loses water and nutrients.
• Recirculation improves resource efficiency and demands stronger monitoring and hygiene.
• Local discharge rules and nutrient recovery should be considered in the SOP.
1
Open · drain-to-waste · operation · simplifies · chemistry · loses
2
Recirculation · improves · resource · efficiency · demands · stronger
3
Local · discharge · rules · nutrient · recovery · should

## Slide 34
HYDROPONIC SYSTEMS
Pump duty must include static and friction head
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: extension.unr.edu
34
ANCHOR: duty point = flow at total dynamic head
• A pump's maximum flow is measured near zero head and is not the operating flow.
• Long narrow tubing, elbows and elevation add resistance.
• Measure delivered channel flow instead of relying on the box label.
1
pump's · maximum · flow · measured · near · zero
2
Long · narrow · tubing · elbows · elevation · resistance
3
Measure · delivered · channel · flow · instead · relying

## Slide 35
HYDROPONIC SYSTEMS
Return design protects against overflow
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: extension.unr.edu
35
ANCHOR: inlet flow ≤ unobstructed drain capacity
• Roots, media and biofilm reduce drainage capacity over time.
• A freeboard and emergency overflow limit water damage.
• Power-off testing reveals siphon and reservoir-capacity hazards.
1
Roots · media · biofilm · reduce · drainage · capacity
2
freeboard · emergency · overflow · limit · water · damage
3
Power-off · testing · reveals · siphon · reservoir-capacity · hazards

## Slide 36
HYDROPONIC SYSTEMS
Redundancy is proportional to crop loss exposure
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
36
ANCHOR: failure detection time × root drying rate
• NFT may require rapid alarm response because exposed roots dry quickly.
• DWC carries more water reserve but depends on aeration.
• Spare pumps, independent air and tested response actions reduce consequence.
1
require · rapid · alarm · response · because · exposed
2
carries · more · water · reserve · depends · aeration
3
Spare · pumps · independent · tested · response · actions

## Slide 37
HYDROPONIC SYSTEMS
Media properties drive irrigation strategy
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: rhs.org.uk
37
ANCHOR: air-filled porosity · water holding · stability
• Coco coir holds water but requires controlled salt management.
• Perlite increases aeration with low mass and low buffering.
• Rockwool is uniform but demands careful wetness control and disposal planning.
Legacy visual reused from original slide 121

## Slide 38
HYDROPONIC SYSTEMS
Food-contact materials need verification
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
38
ANCHOR: compatible plastics + cleanable geometry
• Avoid unknown reused containers that may have held chemicals.
• Opaque reservoirs suppress light-driven algae growth.
• Smooth accessible surfaces make cleaning and inspection more reliable.
1
Avoid · unknown · reused · containers · that · have
2
Opaque · reservoirs · suppress · light-driven · algae · growth
3
Smooth · accessible · surfaces · make · cleaning · inspection

## Slide 39
HYDROPONIC SYSTEMS
A system diagram is an operating control
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
39
ANCHOR: reservoir → pump → crop → return
• Mark flow direction, valves, sampling point and drain route.
• Identify single points of failure and overflow paths.
• The diagram supports training, troubleshooting and maintenance isolation.
1
Mark flow direction, valves, sampling point and drain route.
→
2
Identify single points of failure and overflow paths.
→
3
The diagram supports training, troubleshooting and maintenance isolation.

## Slide 40
03
Water and nutrients
Measure, mix and correct the root-zone chemistry
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
40

## Slide 41
WATER AND NUTRIENTS
Source water sets the starting chemistry
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
41
ANCHOR: alkalinity differs from pH
• pH is the current hydrogen-ion condition; alkalinity resists pH change.
• High bicarbonate water can drive pH upward after correction.
• Record source EC, pH and where relevant alkalinity before formulating.
1
current · hydrogen-ion · condition · alkalinity · resists · change
2
High · bicarbonate · water · drive · upward · after
3
Record · source · where · relevant · alkalinity · before

## Slide 42
WATER AND NUTRIENTS
pH controls chemical availability
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
42
ANCHOR: leafy-green working band commonly ~5.5–6.5
• Outside the operating band, some ions become less available or precipitate.
• Adjust in small increments after nutrients are fully mixed.
• Crop-specific SOPs override a generic band.
1
Outside · operating · band · some · ions · become
2
Adjust · small · increments · after · nutrients · fully
3
Crop-specific · SOPs · override · generic · band

## Slide 43
WATER AND NUTRIENTS
EC is a proxy, not a recipe
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: extension.unr.edu
43
ANCHOR: mS/cm or µS/cm at a stated temperature
• EC increases with dissolved ions from fertiliser and source water.
• Different ion mixtures can produce a similar EC.
• Use the supplier formulation and crop response together with EC.
1
increases · with · dissolved · ions · from · fertiliser
2
Different · mixtures · produce · similar
3
supplier · formulation · crop · response · together · with

## Slide 44
WATER AND NUTRIENTS
Temperature compensation has limits
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: extension.unr.edu
44
ANCHOR: conductivity changes with temperature
• ATC helps standardise meter readings but does not protect warm roots.
• Record solution temperature with pH and EC.
• Compare trends at similar times of day where possible.
1
helps · standardise · meter · readings · does · protect
2
Record · solution · temperature · with
3
Compare · trends · similar · times · where · possible

## Slide 45
WATER AND NUTRIENTS
Two-part nutrients prevent concentrate reactions
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: rhs.org.uk
45
ANCHOR: keep calcium separate from concentrated sulfate/phosphate
• Mix Part A into water before Part B; never combine concentrates directly.
• Allow circulation between additions.
• Precipitate removes nutrients from solution and can block emitters.
1
Mix Part A into water before Part B; never combine concentrates directly.
→
2
Allow circulation between additions.
→
3
Precipitate removes nutrients from solution and can block emitters.

## Slide 46
WATER AND NUTRIENTS
Macronutrients build structure and metabolism
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: rhs.org.uk
46
ANCHOR: N · P · K · Ca · Mg · S
• Nitrogen supports proteins and chlorophyll; imbalance can drive weak lush growth.
• Potassium regulates water balance and enzyme activity.
• Calcium depends strongly on transport to new tissue.
1
Nitrogen · supports · proteins · chlorophyll · imbalance · drive
2
Potassium · regulates · water · balance · enzyme · activity
3
Calcium · depends · strongly · transport · tissue

## Slide 47
WATER AND NUTRIENTS
Micronutrients operate at small concentrations
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: rhs.org.uk
47
ANCHOR: Fe · Mn · B · Zn · Cu · Mo · Cl · Ni
• Trace requirement does not mean optional.
• Excess micronutrients can become toxic quickly.
• pH and chelation influence iron availability.
1
Trace · requirement · does · mean · optional
2
Excess · micronutrients · become · toxic · quickly
3
chelation · influence · iron · availability

## Slide 48
WATER AND NUTRIENTS
Symptoms are patterns, not diagnoses
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: rhs.org.uk
48
ANCHOR: old versus new growth + distribution + roots
• Mobile-element shortages often appear first on older leaves.
• Immobile-element disorders often affect new growth.
• Confirm root health, pH, EC and recent operations before correcting nutrients.
Legacy visual reused from original slide 133

## Slide 49
WATER AND NUTRIENTS
Tip burn can occur with calcium present
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: rhs.org.uk
49
ANCHOR: calcium transport follows transpiration
• Fast inner-leaf growth, high humidity and weak airflow can limit local calcium delivery.
• Raising EC blindly may worsen water uptake.
• Control growth rate, air movement and root conditions.
1
Fast · inner-leaf · growth · high · humidity · weak
2
Raising · blindly · worsen · water · uptake
3
Control · growth · rate · movement · root · conditions

## Slide 50
WATER AND NUTRIENTS
Iron chlorosis needs differential diagnosis
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: rhs.org.uk
50
ANCHOR: interveinal yellowing on young leaves
• High root-zone pH can reduce iron availability.
• Root damage and cold/wet stress can mimic nutrient shortage.
• Correct the limiting condition before adding more concentrate.
1
High · root-zone · reduce · iron · availability
2
Root · damage · cold/wet · stress · mimic · nutrient
3
Correct · limiting · condition · before · adding · more

## Slide 51
WATER AND NUTRIENTS
Dilution calculation prevents overdosing
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
51
ANCHOR: C₁V₁ = C₂V₂
• Use consistent units and confirm the concentrate label.
• Estimate conservatively, mix, measure, then trim.
• Wear required PPE and keep acids/bases labelled and segregated.
1
consistent · units · confirm · concentrate · label
2
Estimate · conservatively · measure · then · trim
3
Wear · required · keep · acids/bases · labelled · segregated

## Slide 52
WATER AND NUTRIENTS
Top-up strategy depends on both water and ions
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: extension.unr.edu
52
ANCHOR: reservoir level + EC trend + crop stage
• Falling level with rising EC suggests water is leaving faster than ions.
• Falling level with falling EC suggests strong nutrient uptake or dilution history.
• Periodic replacement resets selective-ion drift and accumulated residues.
1
Falling · level · with · rising · suggests · water
2
Falling · level · with · falling · suggests · strong
3
Periodic · replacement · resets · selective-ion · drift · accumulated

## Slide 53
WATER AND NUTRIENTS
Meter calibration is part of the measurement
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
53
ANCHOR: known standard → rinse → calibrate → verify
• Use fresh, unexpired standards appropriate to the meter.
• Do not pour used standard back into its bottle.
• Record calibration date, standard value and result.
1
fresh · unexpired · standards · appropriate · meter
2
pour · used · standard · back · into · bottle
3
Record · calibration · date · standard · value · result

## Slide 54
WATER AND NUTRIENTS
Sampling location changes the reading
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
54
ANCHOR: representative, mixed, bubble-free sample
• A dosing point can read very differently before complete mixing.
• Rinse the cup and probe with sample solution.
• Consistent sampling improves trend comparability.
1
dosing · point · read · very · differently · before
2
Rinse · probe · with · sample · solution
3
Consistent · sampling · improves · trend · comparability

## Slide 55
WATER AND NUTRIENTS
pH correction is a controlled chemical task
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
55
ANCHOR: small dose + circulation + remeasurement
• Concentrated acid or alkali can burn skin and roots.
• Add chemical to water as specified; never improvise mixing order.
• Stop if the label, SDS, PPE or correct dosing tool is unavailable.
1
Concentrated · acid · alkali · burn · skin · roots
2
chemical · water · specified · never · improvise · mixing
3
Stop · label · correct · dosing · tool · unavailable

## Slide 56
WATER AND NUTRIENTS
Reservoir sizing buffers change
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: extension.unr.edu
56
ANCHOR: litres per plant and refill frequency
• A larger volume changes temperature and EC more slowly.
• Excess volume adds weight and cleaning burden.
• Keep enough free capacity for return water during power-off tests.
1
larger · volume · changes · temperature · more · slowly
2
Excess · volume · adds · weight · cleaning · burden
3
Keep · enough · free · capacity · return · water

## Slide 57
WATER AND NUTRIENTS
Light exclusion is an algae control
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
57
ANCHOR: photons + nutrients + wet surface = algae opportunity
• Cover reservoirs and unused planting holes.
• Algae competes for oxygen, blocks flow and creates slippery surfaces.
• Clean the root cause rather than relying only on chemical treatment.
1
Cover · reservoirs · unused · planting · holes
2
Algae · competes · oxygen · blocks · flow · creates
3
Clean · root · cause · rather · than · relying

## Slide 58
WATER AND NUTRIENTS
Biofilm changes hydraulics and hygiene
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
58
ANCHOR: surface attachment + organic load + time
• Biofilm can harbour organisms and narrow emitters or channels.
• Inspection targets junctions, dead legs and rough surfaces.
• Cleaning must include physical removal, validated chemistry and rinsing.
1
Biofilm · harbour · organisms · narrow · emitters · channels
2
Inspection · targets · junctions · dead · legs · rough
3
Cleaning · must · include · physical · removal · validated

## Slide 59
04
Crop production
Control nursery, environment, hygiene and crop health
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
59

## Slide 60
CROP PRODUCTION
Crop choice must fit the system envelope
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: rhs.org.uk
60
ANCHOR: cycle time · canopy · root volume · support
• Leafy greens suit short cycles and modest structural support.
• Fruiting crops need longer occupancy, pollination and trellising.
• Marketable yield, not plant count, is the production measure.
1
Leafy · greens · suit · short · cycles · modest
2
Fruiting · crops · need · longer · occupancy · pollination
3
Marketable · yield · plant · count · production · measure

## Slide 61
CROP PRODUCTION
Seed quality affects the whole batch
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: extension.illinois.edu
61
ANCHOR: germination % and uniform emergence
• Record cultivar, lot and sowing date.
• Uniform plugs create more even transplant and harvest timing.
• Separate non-germination from later seedling mortality.
1
Record · cultivar · sowing · date
2
Uniform · plugs · create · more · even · transplant
3
Separate · non-germination · from · later · seedling · mortality

## Slide 62
CROP PRODUCTION
Nursery moisture balances water and oxygen
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
62
ANCHOR: saturated is not synonymous with healthy
• Overwet media reduces aeration and encourages disease.
• Drying interrupts germination and damages fine roots.
• Use clean water delivery and defined transplant acceptance criteria.
1
Overwet · media · reduces · aeration · encourages · disease
2
Drying · interrupts · germination · damages · fine · roots
3
clean · water · delivery · defined · transplant · acceptance

## Slide 63
CROP PRODUCTION
Transplant timing is a root-and-canopy decision
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
63
ANCHOR: established roots + true leaves + intact plug
• Overgrown seedlings suffer root binding and transition stress.
• Weak seedlings create permanent variability in channel performance.
• Reject diseased or mechanically damaged plugs.
1
Overgrown · seedlings · suffer · root · binding · transition
2
Weak · seedlings · create · permanent · variability · channel
3
Reject · diseased · mechanically · damaged · plugs

## Slide 64
CROP PRODUCTION
Light quantity is measured as photons
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
64
ANCHOR: PPFD (µmol·m⁻²·s⁻¹) and DLI
• PPFD describes instantaneous photosynthetic photon flux density.
• DLI integrates PPFD over the photoperiod.
• Uniformity matters because the lowest-light positions limit consistent production.
1
PPFD · describes · instantaneous · photosynthetic · photon · flux
2
integrates · PPFD · over · photoperiod
3
Uniformity · matters · because · lowest-light · positions · limit

## Slide 65
CROP PRODUCTION
Daily Light Integral links intensity and time
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
65
ANCHOR: DLI = PPFD × seconds ÷ 1,000,000
• Longer photoperiod can partly compensate for lower intensity within crop limits.
• More photons can raise cooling and electricity demand.
• Measure at canopy height across the growing area.
1
Longer · photoperiod · partly · compensate · lower · intensity
2
More · photons · raise · cooling · electricity · demand
3
Measure · canopy · height · across · growing · area

## Slide 66
CROP PRODUCTION
Air temperature and humidity shape demand
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
66
ANCHOR: vapour-pressure deficit (VPD)
• Very low evaporative demand can reduce nutrient transport to fast-growing tissue.
• Very high demand can exceed root water supply and close stomata.
• Use crop response with environmental trends, not temperature alone.
1
Very · evaporative · demand · reduce · nutrient · transport
2
Very · high · demand · exceed · root · water
3
crop · response · with · environmental · trends · temperature

## Slide 67
CROP PRODUCTION
Airflow is a boundary-layer control
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
67
ANCHOR: leaf movement without mechanical stress
• Gentle circulation supports gas exchange and canopy uniformity.
• Dead zones retain humidity and favour disease.
• Excess wind raises water demand and causes abrasion.
1
Gentle · circulation · supports · exchange · canopy · uniformity
2
Dead · zones · retain · humidity · favour · disease
3
Excess · wind · raises · water · demand · causes

## Slide 68
CROP PRODUCTION
Integrated pest management starts with exclusion
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
68
ANCHOR: prevent → monitor → identify → intervene → verify
• Screen openings and inspect incoming plants/materials.
• Use sticky cards and crop scouting to detect change.
• Choose interventions that are lawful, label-compliant and compatible with harvest.
1
Screen openings and inspect incoming plants/materials.
→
2
Use sticky cards and crop scouting to detect change.
→
3
Choose interventions that are lawful, label-compliant and compatible with harvest.

## Slide 69
CROP PRODUCTION
Sticky cards are trend tools
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
69
ANCHOR: standard location + interval + count
• Card colour and placement affect which flying pests are captured.
• Counts are comparable only with a consistent method.
• A trap result must be paired with crop inspection and correct identification.
1
Card · colour · placement · affect · which · flying
2
Counts · comparable · only · with · consistent · method
3
trap · result · must · paired · with · crop

## Slide 70
CROP PRODUCTION
Root inspection is non-negotiable
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
70
ANCHOR: colour · odour · firmness · branching
• Healthy roots are generally light-coloured and firm, with crop-dependent variation.
• Brown slimy roots and off-odour require rapid investigation.
• Inspect the least vigorous plants and the return end, not only the best canopy.
Legacy visual reused from original slide 133

## Slide 71
CROP PRODUCTION
Harvest hygiene protects ready-to-eat produce
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
71
ANCHOR: clean hands/tools + cleanable surfaces + lot traceability
• Separate dirty maintenance tools from harvest equipment.
• Remove damaged or contaminated produce from the marketable lot.
• Record harvest date, crop/lot, quantity and responsible operator.
1
Separate · dirty · maintenance · tools · from · harvest
2
Remove · damaged · contaminated · produce · from · marketable
3
Record · harvest · date · crop/lot · quantity · responsible

## Slide 72
CROP PRODUCTION
Housekeeping controls slips and contamination
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: tertiarycourses.com.sg
72
ANCHOR: dry walkways + contained chemicals + clear access
• Leaks are production deviations and safety hazards.
• Electrical connections need dry, protected routing.
• Emergency access, labels and SDS must remain visible.
1
Leaks · production · deviations · safety · hazards
2
Electrical · connections · need · protected · routing
3
Emergency · access · labels · must · remain · visible

## Slide 73
CROP PRODUCTION
Cleaning is not the same as disinfection
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
73
ANCHOR: soil removal precedes disinfectant contact
• Organic residue shields organisms and consumes disinfectant.
• Correct concentration, contact time and material compatibility are required.
• Rinsing and drying requirements follow the product label/SOP.
1
Organic · residue · shields · organisms · consumes · disinfectant
2
Correct · concentration · contact · time · material · compatibility
3
Rinsing · drying · requirements · follow · product · label/SOP

## Slide 74
CROP PRODUCTION
Maintenance preserves control capability
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: tertiarycourses.com.sg
74
ANCHOR: inspect → clean → replace → function-test → record
• Pumps, air stones, tubing, filters, probes and timers have different failure modes.
• A spare part is useful only if compatible and accessible.
• Return equipment to service only after a functional verification.
1
Pumps, air stones, tubing, filters, probes and timers have different failure modes.
→
2
A spare part is useful only if compatible and accessible.
→
3
Return equipment to service only after a functional verification.

## Slide 75
05
Singapore hydroponics
Current policy, farms, productivity and technology cases
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
75

## Slide 76
SINGAPORE HYDROPONICS
Singapore Food Story 2 resets the context
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: mse.gov.sg
76
ANCHOR: 2035 capacity targets—20% fibre, 30% protein
• The current policy focuses on resilient production capacity and commercial viability.
• Previous national framing has been superseded by the current 2035 capacity targets.
• Hydroponics contributes mainly to the fibre category through vegetables.
Chart: 
| Fibre | Protein
2025 local output (%) | 8 | 25
2035 capacity target (%) | 20 | 30

## Slide 77
SINGAPORE HYDROPONICS
2025 output shows the remaining fibre gap
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
77
ANCHOR: about 8% fibre and 25% protein in 2025
• Local output is only one layer of Singapore's food-resilience strategy.
• Productivity, demand, import diversification and stockpiling interact.
• A technical system must still produce saleable crops at viable cost.
Chart: 
| Fibre | Protein
Remaining percentage-point gap to 2035 target | 12 | 5

## Slide 78
SINGAPORE HYDROPONICS
Vegetable productivity rose in 2025
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
78
ANCHOR: 231.4 → 253.3 tonnes/ha/year
• SFA reported roughly a 10% increase in farm productivity.
• Area-normalised output supports comparison but does not reveal energy or cost.
• Pair yield with grade-out, input use, labour and downtime.
Chart: 
| 2024 | 2025
Vegetable farm productivity (t/ha/year) | 231.4 | 253.3

## Slide 79
SINGAPORE HYDROPONICS
ComCrop demonstrates rooftop hybrid production
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
79
ANCHOR: rooftop hydroponics + sunlight + supplemental light
• SFA describes ComCrop as Singapore's first commercial rooftop farm, established in 2011.
• Sensors support monitoring of water, light and nutrient conditions.
• Manual transplanting, harvesting and cleaning remain important operations.
Legacy visual reused from original slide 46

## Slide 80
SINGAPORE HYDROPONICS
Sustenir compresses production into controlled space
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
80
ANCHOR: NFT + vertical layers + controlled environment
• SFA describes recirculating NFT with temperature, humidity and CO₂ control.
• The farm page reports 3.2 tonnes of lettuce from 54 m² and over 90 tonnes/year.
• Treat site figures as reported case data, not universal performance.
1
describes · recirculating · with · temperature · humidity · control
2
farm · page · reports · tonnes · lettuce · from
3
Treat · site · figures · reported · case · data

## Slide 81
SINGAPORE HYDROPONICS
Singrow targets temperate crops in the tropics
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: enterprise.nus.edu.sg
81
ANCHOR: cultivar + climate control + automation
• The NUS Enterprise case describes proprietary hydroponic strawberries.
• Computer vision, robotics and crop genetics form one production system.
• Higher-value crops may justify complexity that leafy greens cannot.
1
Enterprise · case · describes · proprietary · hydroponic · strawberries
2
Computer · vision · robotics · crop · genetics · form
3
Higher-value · crops · justify · complexity · that · leafy

## Slide 82
SINGAPORE HYDROPONICS
Greenphyto signals a scale-and-automation bet
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: businesstimes.com.sg
82
ANCHOR: reported 23 m chambers and up to 2,000 t/year
• The Business Times reported an S$80 million multi-storey hydroponic facility in January 2026.
• The report describes automated seeding, dosing, crop movement and climate control.
• Capacity and company claims must be distinguished from verified realised output.
1
Business · Times · reported · S$80 · million · multi-storey
2
report · describes · automated · seeding · dosing · crop
3
Capacity · company · claims · must · distinguished · from

## Slide 83
SINGAPORE HYDROPONICS
Digital twins turn operations into models
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: businesstimes.com.sg
83
ANCHOR: sensor state → model → prediction → action
• A digital twin is useful only when sensors are calibrated and the model matches the crop process.
• Prediction can support harvest planning, fault detection and energy optimisation.
• Human verification remains necessary when biology departs from the model.
1
A digital twin is useful only when sensors are calibrated and the model matches the crop process.
→
2
Prediction can support harvest planning, fault detection and energy optimisation.
→
3
Human verification remains necessary when biology departs from the model.

## Slide 84
SINGAPORE HYDROPONICS
Automation changes the job, not the biology
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: businesstimes.com.sg
84
ANCHOR: actuators still depend on trustworthy measurements
• Automated dosing magnifies a bad probe or wrong setpoint.
• Alarms require ownership, escalation and tested response time.
• Operators need crop observation plus technical troubleshooting skills.
1
Automated · dosing · magnifies · probe · wrong · setpoint
2
Alarms · require · ownership · escalation · tested · response
3
Operators · need · crop · observation · plus · technical

## Slide 85
SINGAPORE HYDROPONICS
ACT Fund 2 supports capability transformation
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
85
ANCHOR: new S$70m tranche from 2026
• SFA lists capability upgrading, technology adoption and standards pathways.
• A grant does not remove the need for business and technical feasibility.
• Define measurable production and capability outcomes before procurement.
1
lists · capability · upgrading · technology · adoption · standards
2
grant · does · remove · need · business · technical
3
Define · measurable · production · capability · outcomes · before

## Slide 86
SINGAPORE HYDROPONICS
SG GAP connects production with assurance
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
86
ANCHOR: food safety + quality + environmental + worker welfare controls
• Good agricultural practice depends on documented, repeatable controls.
• Records support traceability and corrective action.
• Certification scope and current requirements must be checked with SFA/standards sources.
1
Good · agricultural · practice · depends · documented · repeatable
2
Records · support · traceability · corrective · action
3
Certification · scope · current · requirements · must · checked

## Slide 87
SINGAPORE HYDROPONICS
Land productivity alone can mislead
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
87
ANCHOR: yield/m² must be read with kWh, labour, water and grade-out
• Vertical stacking can raise output per floor area.
• Lighting, cooling, pumping and dehumidification add operating load.
• A resilient farm optimises the whole system, not a single headline metric.
1
Vertical · stacking · raise · output · floor · area
2
Lighting · cooling · pumping · dehumidification · operating · load
3
resilient · farm · optimises · whole · system · single

## Slide 88
SINGAPORE HYDROPONICS
Tropical heat is a root-zone design input
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
88
ANCHOR: heat gain → warmer solution → lower oxygen margin
• Shade, insulation, reservoir location and operating time influence heat load.
• Cooling can protect crops but adds capital and energy cost.
• Measure the actual daily temperature profile before choosing controls.
1
Shade · insulation · reservoir · location · operating · time
2
Cooling · protect · crops · adds · capital · energy
3
Measure · actual · daily · temperature · profile · before

## Slide 89
SINGAPORE HYDROPONICS
Farm economics start with marketable yield
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
89
ANCHOR: revenue = saleable mass × realised price
• High biological yield can coexist with poor grade-out or weak demand.
• Cycle time and space occupancy affect annual throughput.
• Include packaging, logistics, rejects, energy, labour and downtime.
1
High · biological · yield · coexist · with · poor
2
Cycle · time · space · occupancy · affect · annual
3
Include · packaging · logistics · rejects · energy · labour

## Slide 90
SINGAPORE HYDROPONICS
Resilience needs more than local farms
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: mse.gov.sg
90
ANCHOR: local capacity + diversified imports + stockpiles + partnerships
• Current Singapore policy uses multiple food-security strategies.
• Hydroponics is a targeted production tool, not a universal substitute for imports.
• System choice should be matched to crops Singapore can produce competitively.
1
Current Singapore policy uses multiple food-security strategies.
→
2
Hydroponics is a targeted production tool, not a universal substitute for imports.
→
3
System choice should be matched to crops Singapore can produce competitively.

## Slide 91
06
Farm tour activity
Observe MEOD Farm using evidence-based checklists
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
91

## Slide 92
—
Lunch break
Resume at the farm-tour assembly point stated by the trainer
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
92

## Slide 93
FARM TOUR ACTIVITY
Observe flow before judging appearance
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
93
ANCHOR: trace reservoir → delivery → root zone → return
• Identify the system boundary and where water can leave it.
• Locate measurement, dosing, filtration and overflow points.
• Record observations; do not touch equipment without permission.
Visual: generated for this course

## Slide 94
FARM TOUR ACTIVITY
Read the crop as a spatial pattern
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
94
ANCHOR: inlet/middle/return + upper/lower tier
• Uniform symptoms suggest a shared input; local symptoms suggest position-specific causes.
• Compare canopy colour, size and density across the system.
• Photographs require farm permission and must avoid faces or confidential displays.
1
Uniform · symptoms · suggest · shared · input · local
2
Compare · canopy · colour · size · density · across
3
Photographs · require · farm · permission · must · avoid

## Slide 95
FARM TOUR ACTIVITY
Audit water and nutrient controls
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
95
ANCHOR: instrument + setpoint + frequency + response
• Ask where and when pH, EC and temperature are measured.
• Look for calibration, dosing and corrective-action records.
• Distinguish observed evidence from an operator explanation.
1
where · when · temperature · measured
2
Look · calibration · dosing · corrective-action · records
3
Distinguish · observed · evidence · from · operator · explanation

## Slide 96
FARM TOUR ACTIVITY
Audit WSH and food-safety controls
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: tertiarycourses.com.sg
96
ANCHOR: hazard → existing control → residual risk
• Observe wet floors, electrical routing, chemical storage and manual handling.
• Look for clean/dirty zoning and harvest-tool control.
• Escalate urgent hazards to the trainer; never intervene in machinery.
1
Observe · floors · electrical · routing · chemical · storage
2
Look · clean/dirty · zoning · harvest-tool · control
3
Escalate · urgent · hazards · trainer · never · intervene

## Slide 97
FARM TOUR ACTIVITY
Map preventive maintenance
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
97
ANCHOR: asset ID + interval + completion + function test
• Check pumps, filters, air delivery, sensors, lighting and structural supports.
• Ask how failure is detected and who responds.
• Look for spare-part readiness and documented return-to-service tests.
1
Check · pumps · filters · delivery · sensors · lighting
2
failure · detected · responds
3
Look · spare-part · readiness · documented · return-to-service · tests

## Slide 98
FARM TOUR ACTIVITY
Evaluate pest management evidence
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
98
ANCHOR: monitoring location + count trend + intervention record
• Identify exclusion barriers, scouting routines and sticky-card placement.
• Ask how pests are identified before treatment.
• Confirm interventions respect label, food-safety and pre-harvest requirements.
1
Identify · exclusion · barriers · scouting · routines · sticky-card
2
pests · identified · before · treatment
3
Confirm · interventions · respect · label · food-safety · pre-harvest

## Slide 99
FARM TOUR ACTIVITY
Separate claim, observation and inference
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
99
ANCHOR: C/O/I notation
• Claim: what the guide/operator says.
• Observation: what you directly see, measure or read.
• Inference: your explanation, labelled as provisional until verified.
1
Claim · what · guide/operator · says
2
Observation · what · directly · measure · read
3
Inference · your · explanation · labelled · provisional · until

## Slide 100
FARM TOUR ACTIVITY
Farm-tour evidence is a checklist package
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
100
ANCHOR: completed PDF + permitted photos + one flow sketch
• The activity PDF defines the required evidence.
• Use concise factual notes with location and time.
• Submit no personal data, trade secrets or unsafe photographs.
1
activity · defines · required · evidence
2
concise · factual · notes · with · location · time
3
Submit · personal · data · trade · secrets · unsafe

## Slide 101
07
Hydroponics kit practice
Commission, verify and return a kit to a controlled state
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
101

## Slide 102
HYDROPONICS KIT PRACTICE
Kit readiness is an acceptance state
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
102
ANCHOR: clean · intact · stable · leak-free · electrically safe
• A visual inspection occurs before water or power is applied.
• Tubing must be secured without kinks and returns must be unobstructed.
• Reject damaged cables, unknown containers or unstable structures.
1
visual · inspection · occurs · before · water · power
2
Tubing · must · secured · without · kinks · returns
3
Reject · damaged · cables · unknown · containers · unstable

## Slide 103
HYDROPONICS KIT PRACTICE
Flow verification uses evidence
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
103
ANCHOR: every site wet + return stable + no overflow
• Observe the last planting site, not only the first.
• Confirm pump noise and vibration are normal for the unit.
• A timed-volume check can quantify delivered flow where required.
1
Observe · last · planting · site · only · first
2
Confirm · pump · noise · vibration · normal · unit
3
timed-volume · check · quantify · delivered · flow · where

## Slide 104
HYDROPONICS KIT PRACTICE
A baseline precedes correction
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
104
ANCHOR: source water pH/EC/temperature recorded first
• Baseline data separates source-water contribution from added nutrients.
• Use clean labelled tools to avoid cross-contamination.
• The Learner Guide contains the detailed sequence and safety checks.
1
Baseline · data · separates · source-water · contribution · from
2
clean · labelled · tools · avoid · cross-contamination
3
Learner · Guide · contains · detailed · sequence · safety

## Slide 105
HYDROPONICS KIT PRACTICE
Mixing order protects chemistry
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
105
ANCHOR: water → A → circulate → B → circulate → measure
• Concentrates must never contact each other directly.
• The final EC is verified against the activity setpoint supplied by the trainer.
• Any deviation is corrected incrementally and recorded.
1
Concentrates must never contact each other directly.
→
2
The final EC is verified against the activity setpoint supplied by the trainer.
→
3
Any deviation is corrected incrementally and recorded.

## Slide 106
HYDROPONICS KIT PRACTICE
pH adjustment uses a stop condition
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
106
ANCHOR: no label/SDS/PPE = no dosing
• Use the trainer-provided product and dedicated dosing tool only.
• Add small amounts, circulate and remeasure.
• Never return excess chemical to the stock container.
1
trainer-provided · product · dedicated · dosing · tool · only
2
small · amounts · circulate · remeasure
3
Never · return · excess · chemical · stock · container

## Slide 107
HYDROPONICS KIT PRACTICE
Transplant acceptance protects uniformity
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
107
ANCHOR: intact plug + healthy root + centred support + stable crown
• Roots should contact moisture without burying the crown.
• Remove weak or diseased seedlings from the production batch.
• Plant labels preserve cultivar and date traceability.
1
Roots · should · contact · moisture · without · burying
2
Remove · weak · diseased · seedlings · from · production
3
Plant · labels · preserve · cultivar · date · traceability

## Slide 108
HYDROPONICS KIT PRACTICE
Power-off behaviour is part of commissioning
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
108
ANCHOR: no siphon overflow + reservoir contains return volume
• Simulated power loss exposes drainage and restart behaviour.
• Restart must restore delivery to every site.
• Do not conduct the test where electrical or spill controls are inadequate.
1
Simulated · power · loss · exposes · drainage · restart
2
Restart · must · restore · delivery · every · site
3
conduct · test · where · electrical · spill · controls

## Slide 109
HYDROPONICS KIT PRACTICE
A correction log closes the loop
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
109
ANCHOR: before → action → after → operator → time
• Record the reason and exact quantity added.
• Allow adequate mixing before the after-reading.
• Escalate if the value does not respond as expected.
1
Record · reason · exact · quantity · added
2
Allow · adequate · mixing · before · after-reading
3
Escalate · value · does · respond · expected

## Slide 110
HYDROPONICS KIT PRACTICE
Root-zone diagnosis starts below the canopy
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: sfa.gov.sg
110
ANCHOR: roots + flow + temperature + chemistry
• Leaf symptoms alone can lead to the wrong correction.
• Inspect for obstruction, low aeration, warmth and odour.
• Isolate suspect plants and protect the shared reservoir where required by SOP.
Visual: generated for this course

## Slide 111
HYDROPONICS KIT PRACTICE
Cleaning returns the kit to a controlled state
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
111
ANCHOR: drain → remove residue → clean → rinse → dry → store
• Electrical components are isolated from water.
• Disassemble only parts approved by the equipment SOP.
• Final evidence shows a dry, complete kit with chemicals secured.
1
Electrical components are isolated from water.
→
2
Disassemble only parts approved by the equipment SOP.
→
3
Final evidence shows a dry, complete kit with chemicals secured.

## Slide 112
HYDROPONICS KIT PRACTICE
Practice evidence maps to A1–A4
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: tertiarycourses.com.sg
112
ANCHOR: prepare · operate · comply · maintain
• A1: materials and equipment ready.
• A2: system operates to target with measured evidence.
• A3: WSH, food safety and housekeeping controls observed.
• A4: cleaning, maintenance check and storage completed.
1
A1: materials and equipment ready
2
A2: system operates to target with measured evidence
3
A3: WSH, food safety and housekeeping controls observed
4
A4: cleaning, maintenance check and storage completed

## Slide 113
08
Aquaponics theory
Balance fish, microbes, plants and water quality
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
113

## Slide 114
AQUAPONICS THEORY
Aquaponics couples two biological processes
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
114
ANCHOR: fish waste → nitrification → plant uptake
• Fish produce ammonia-containing waste.
• Nitrifying microbes convert ammonia to nitrite and then nitrate.
• Plants remove nutrients, while water returns to the culture system.
Visual: generated for this course

## Slide 115
AQUAPONICS THEORY
The nitrogen cycle has toxic intermediates
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
115
ANCHOR: NH₃/NH₄⁺ → NO₂⁻ → NO₃⁻
• Unionised ammonia toxicity rises with pH and temperature.
• Nitrite interferes with oxygen transport in fish.
• Nitrate is less acutely toxic but still requires system balance.
1
Unionised ammonia toxicity rises with pH and temperature.
→
2
Nitrite interferes with oxygen transport in fish.
→
3
Nitrate is less acutely toxic but still requires system balance.

## Slide 116
AQUAPONICS THEORY
Three living groups share one water loop
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
116
ANCHOR: fish · microbes · plants
• A setpoint suitable for plants alone may harm fish or biofilter microbes.
• Feeding rate drives nutrient loading and oxygen demand.
• Management aims for an acceptable compromise, not a single-species optimum.
1
setpoint · suitable · plants · alone · harm · fish
2
Feeding · rate · drives · nutrient · loading · oxygen
3
Management · aims · acceptable · compromise · single-species · optimum

## Slide 117
AQUAPONICS THEORY
pH is a compromise variable
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
117
ANCHOR: fish health + nitrification + nutrient availability
• Nitrification tends to acidify the system over time.
• Very high pH can increase toxic unionised ammonia fraction.
• Corrections must be gradual and compatible with all organisms.
1
Nitrification · tends · acidify · system · over · time
2
Very · high · increase · toxic · unionised · ammonia
3
Corrections · must · gradual · compatible · with · organisms

## Slide 118
AQUAPONICS THEORY
Dissolved oxygen supports fish, roots and biofilter
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
118
ANCHOR: three simultaneous oxygen demands
• Warm water and high feeding increase risk.
• Aeration failure can become an emergency.
• Independent air delivery and alarms may be justified by stock value and response time.
1
Warm · water · high · feeding · increase · risk
2
Aeration · failure · become · emergency
3
Independent · delivery · alarms · justified · stock · value

## Slide 119
AQUAPONICS THEORY
Solids management precedes mineralisation
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
119
ANCHOR: settle/filter solids before they foul roots
• Uneaten feed and faecal solids consume oxygen during decomposition.
• Mechanical separation reduces deposition in plant channels.
• Captured nutrients may be mineralised in a controlled process.
1
Uneaten feed and faecal solids consume oxygen during decomposition.
→
2
Mechanical separation reduces deposition in plant channels.
→
3
Captured nutrients may be mineralised in a controlled process.

## Slide 120
AQUAPONICS THEORY
Biofilters need surface area and flow
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
120
ANCHOR: attached nitrifiers + oxygenated water + alkalinity
• New systems require cycling before full fish loading.
• Disinfectants and sudden chemistry changes can damage the microbial community.
• Monitor ammonia and nitrite during startup and after disturbances.
1
systems · require · cycling · before · full · fish
2
Disinfectants · sudden · chemistry · changes · damage · microbial
3
Monitor · ammonia · nitrite · during · startup · after

## Slide 121
AQUAPONICS THEORY
Feeding rate is the nutrient input
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
121
ANCHOR: feed mass/day links fish biomass to plant area
• Overfeeding raises waste, oxygen demand and water-quality risk.
• Underfeeding limits fish growth and plant nutrients.
• Use species-, feed- and system-specific design guidance.
1
Overfeeding · raises · waste · oxygen · demand · water-quality
2
Underfeeding · limits · fish · growth · plant · nutrients
3
species- · feed- · system-specific · design · guidance

## Slide 122
AQUAPONICS THEORY
Decoupled aquaponics separates optimisation
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
122
ANCHOR: controlled transfer between fish and plant loops
• A decoupled design can protect fish from crop-specific corrections.
• It adds tanks, controls, monitoring and operating complexity.
• The value depends on production goals and operator capability.
1
decoupled · design · protect · fish · from · crop-specific
2
adds · tanks · controls · monitoring · operating · complexity
3
value · depends · production · goals · operator · capability

## Slide 123
AQUAPONICS THEORY
Biosecurity spans water, animals and plants
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
123
ANCHOR: quarantine + source control + sanitation + records
• Do not transfer water, nets or plants between systems without control.
• Fish health and food-safety obligations differ from plant-only hydroponics.
• Mortality, treatment and water-quality records support investigation.
1
transfer · water · nets · plants · between · systems
2
Fish · health · food-safety · obligations · differ · from
3
Mortality · treatment · water-quality · records · support · investigation

## Slide 124
AQUAPONICS THEORY
Hydroponics and aquaponics solve different constraints
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
124
ANCHOR: formulated nutrients versus biological nutrient generation
• Hydroponics offers direct nutrient formulation and easier crop isolation.
• Aquaponics creates coupled biological value and coupled risk.
• Choose based on production objective, market, regulation and operational skill.
1
Hydroponics · offers · direct · nutrient · formulation · easier
2
Aquaponics · creates · coupled · biological · value · coupled
3
Choose · based · production · objective · market · regulation

## Slide 125
AQUAPONICS THEORY
Aquaponics troubleshooting follows the loop
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
125
ANCHOR: fish → feed → oxygen → ammonia → biofilter → plant
• Start with animal behaviour and critical water quality.
• Trace flow and aeration before adding chemicals.
• Correct the cause while protecting the most sensitive organism.
1
Start with animal behaviour and critical water quality.
→
2
Trace flow and aeration before adding chemicals.
→
3
Correct the cause while protecting the most sensitive organism.

## Slide 126
COURSE CLOSE
Assessment briefing
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: tertiarycourses.com.sg
126
ANCHOR: WA-SAQ 30 min + PP 30 min
• Read the candidate instructions before responding.
• Use the equipment and evidence checklist specified by the assessor.
• Competent / Not Yet Competent decisions follow the approved criteria.
1
Read the candidate instructions before responding.
→
2
Use the equipment and evidence checklist specified by the assessor.
→
3
Competent / Not Yet Competent decisions follow the approved criteria.

## Slide 127
COURSE CLOSE
Assessment and appeal flow
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: tertiarycourses.com.sg
127
ANCHOR: attempt → assessor decision → feedback → reassessment/appeal
• Ask for clarification only on instructions, not model answers.
• Sign the acknowledgement after feedback.
• Follow the provider's documented appeal route where needed.
1
Ask for clarification only on instructions, not model answers.
→
2
Sign the acknowledgement after feedback.
→
3
Follow the provider's documented appeal route where needed.

## Slide 128
COURSE CLOSE
Digital attendance and TRAQOM
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: tertiarycourses.com.sg
128
ANCHOR: identity + attendance + feedback records
• Complete attendance using the provider's authorised channel.
• Do not share login or Singpass credentials.
• Submit course feedback after the assessment process.
1
Complete · attendance · using · provider's · authorised · channel
2
share · login · Singpass · credentials
3
Submit · course · feedback · after · assessment · process

## Slide 129
COURSE CLOSE
Thank you
TGS-2025053916 · Basic Urban Farming with Hydroponics
© 2026 Tertiary Infotech Academy Pte Ltd
Source: tertiarycourses.com.sg
129
ANCHOR: control the root zone, verify the evidence
• Observe the whole water–root–canopy loop.
• Operate to SOP and stop when controls are missing.
• Use measurements and records to improve the next crop cycle.
1
Observe · whole · water–root–canopy · loop
2
Operate · stop · when · controls · missing
3
measurements · records · improve · next · crop · cycle